## Slide 1
Controlled Kernel Launch for Dynamic Parallelism in GPUs
Xulong Tang, Ashutosh Pattnaik, Huaipan Jiang,
Onur Kayiran, Adwait Jog, Sreepathi Pai, Mohamed Ibrahim,
Mahmut T. Kandemir, Chita R. Das
HPCA - 23

## Slide 2: Irregularity of Applications
Irregular applications
  Molecular dynamics
  Earthquake simulation
  Weather simulations
  Economics
Most of these applications
use GPUs for acceleration.
Are GPUs being used efficiently?
Image source:
http://www.nature.com/nature/journal/v516/n7530/fig_tab/nature13768_SF5.html
https://en.wikipedia.org/wiki/Weather_Research_and_Forecasting_Model
http://www.tibetnature.net/en/massive-fast-moving-structure-seen-beneath-tibetan-plateau-in-earthquake-simulation-study/
https://hgchicago.org/courses/advanced-courses/economic-science/

## Slide 3: Irregularity: Source of GPU Inefficiency
Imbalanced workload among GPU threads
  Thread-1 (T1) undertakes more computations than other threads.
Underutilized hardware resources
  Threads, register files, shared memory, etc.
T1
T3
T2
T4
PE1
PE2
PE3
Execution time
PE4
Idle

## Slide 4: Dynamic Parallelism in GPUs
PE1
PE2
PE3
Execution Time
PE4
PE1
PE2
PE3
Execution Time
PE4
Dynamic parallelism (DP)
  Allow applications to launch kernels at the device (GPU) side, without CPU intervention.
Advantages
  High GPU occupancy
  Dynamic load balancing
  Supports recursive parallel applications
Child Kernel
Child Kernel
Child Kernel
Child Kernel
Child Kernel
Child Kernel
Child Kernel
Parent Kernel
Application
Parent Kernel
Threads
T2
T3
…
T1
…
…
…
…
Is Dynamic Parallelism the solution for all
irregular applications?
Idle

## Slide 5
Performance
Workload distribution ratio between parent and child
Launching child kernels improves parallelism.
More child kernels increase overhead, and do not improve parallelism further, due to hardware limits.
All work in
parent kernel
All work in
child kernels
Performance peak
There is no free lunch!
Dynamic Parallelism in GPUs

## Slide 6: Executive Summary
Dynamic Parallelism improves parallelism for irregular applications running on GPUs.
However, aggressively launching child kernels without knowledge of hardware state degrades performance.
DP needs to make smarter decisions on how many child kernels should be launched.
Our proposal: SPAWN, a runtime framework,
which uses GPU hardware state to decide
how many kernels to launch

## Slide 7
Introduction
Background
Characterization
Our proposal: SPAWN
Evaluation
Conclusions
Outline

## Slide 8: Background: DP Usage in Applications
parent (type *workload){
2. …
3. if (local_workload > THRESHOLD){
4. child<<< c_grid, c_cta, shmem, c_stream>>> 5. else
6. while(local_workload){…}
7. …}
Three key parameters related to child kernel.
  Workload distribution
  ratio (THRESHOLD)
  Child kernel dimension (c_grid, c_cta)
  Child kernel execution order (c_stream)
1. int main(){
2. …
parent<<< p_grid, p_cta>>>(type *workload);
…}
1. __global__ void child(*c_workload){
2. …
3. }
Host code
Parent kernel
Child kernel

## Slide 9
Application
Host
(CPU)
1
Grid Management Unit (GMU)
K3
K2
K1
Hardware Work
Queues
Stream Queue Management (SQM)
K1
K2
K3
Software Work
Queues
Software Support
Hardware Support
2
3
4
5
PE
CTA scheduler
PE
PE
PE
Runtime APIs
Device Runtime APIs
Background: Hardware Support for DP
6

## Slide 10
Introduction
Background
Characterization
Our proposal: SPAWN
Evaluation
Conclusions
Outline

## Slide 11
Three key parameters.
  Workload distribution ratio, child kernel dimension, child kernel sequence
Observations
  Workload distribution is very important.
  Preferred workload distribution ratio varies for different applications and inputs.
Best offline-search: peak performance through manually varying the workload distribution ratio (THRESHOLD).
Baseline-DP: offload most computations by launching child kernels.
Characterization of DP Applications
BFS-citation
Chart: Percentage of workload being offloaded to child kernels
| 0.01 | 0.05 | 0.13 | 0.28000000000000003 | 0.35 | 0.53 | 0.85
Simulator | 0.9877 | 1.0329 | 1.0372 | 1.0104 | 0.87609 | 0.4598 | 0.13162
K20m | 0.98267 | 1.0119 | 1.0471 | 0.80095 | 0.64807 | 0.057886 | 0.057886
MM-small
Chart: Percentage of workload being offloaded to child kernels
| 1.171875E-2 | 3.3203125E-2 | 0.25 | 0.3125 | 0.48828125 | 0.740234375 | 0.89453125
ss | 1.0024 | 1.0299 | 1.3271 | 1.5611 | 1.795 | 2.0568 | 2.4348
hw | 1.0554 | 1.0649 | 1.2046 | 1.2946 | 1.4499 | 1.6941 | 2.3013
BFS-graph500
Chart: Percentage of workload being offloaded to child kernels
| 0.01 | 0.05 | 0.1 | 0.33 | 0.57999999999999996 | 0.77093772298632102 | 0.90560067530227328
Simulator | 1.0787 | 1.3231 | 1.4764 | 1.3437 | 1.2297 | 0.91271 | 0.8617
K20m | 0.97569 | 1.0631 | 1.2005 | 1.5755 | 1.8592 | 1.2964 | 0.91342
Most work done by parent threads
Most work done by child kernels

## Slide 12
Launch overhead: from invoking API to kernels being pushed into GMU and ready to start execution.
Queuing latency: Kernels waiting in GMU due to the hardware limitations.
  Maximum number of concurrently running kernels.
  Maximum number of concurrently running CTAs.
  Available hardware resources.
6
3
4
+
+
Overheads
Application
Host
(CPU)
1
Grid Management Unit (GMU)
K3
K2
K1
Hardware Work
Queues
Stream Queue Management (SQM)
K1
K2
K3
Software Work
Queues
Software Support
Hardware Support
2
5
PE
CTA scheduler
PE
PE
PE
Runtime APIs
Device Runtime APIs
3
4
6

## Slide 13: Workload Distribution
Parent Kernel
Parent Kernel Waiting
Launch Overhead
HWQ
CTAparent
HWQ
Ⅰ
CTAparent
Time
Parent Kernel
Child Kernel
Too many child kernels.

## Slide 14: Workload Distribution
Parent Kernel
Parent Kernel
Parent Kernel Waiting
Launch Overhead
A
HWQ
CTAparent
HWQ
Launch Overhead
Ⅰ
Ⅱ
CTAparent
HWQ
HWQ
Time
Parent Kernel
Child Kernel
CTAparent
CTAparent
Not enough child kernels.
Too many child kernels.

## Slide 15: Workload Distribution
Parent Kernel
Child Kernel
Parent Kernel
Parent Kernel
Parent Kernel Waiting
Launch Overhead
A
HWQ
CTAparent
B
HWQ
Parent Kernel
Launch Overhead
Ⅰ
Ⅱ
Launch Overhead
CTAparent
Ⅲ
HWQ
HWQ
HWQ
HWQ
Time
CTAparent
CTAparent
CTAparent
CTAparent
Not enough child kernels.
Too many child kernels.
Important to decide how many child kernels to launch

## Slide 16
Chart: Speedup
| AMR | BFS-citation | BFS-graph500 | SSSP-citation | SSSP-graph500 | JOIN-uniform | JOIN-gaussion | Mandel | GC-citation | GC-graph500 | MM-small | MM-large | SA-thaliana | Geomean
Baseline-DP | 0.51021 | 0.4598 | 0.8617 | 1.0787 | 2.441 | 0.3848 | 0.25747 | 1.4048 | 1.0056 | 0.99506 | 2.4348 | 3.2779 | 4.3765 | 1.0759
Offline-Search | 2.0982 | 1.0412 | 1.492 | 1.1839 | 2.9927 | 1.3566 | 1.0418 | 1.9745 | 1.0203 | 1.0637 | 2.4348 | 3.9313 | 4.3765 | 1.752
(best)
Average speedup of best Offline-Search scenario
        over non-DP implementation: 1.73x
        over Baseline-DP implementation: 1.61x
Opportunities

## Slide 17: Our goal
Improving hardware resource utilization of DP applications
Preventing the application from reaching the hardware limitations
Dynamically controlling the performance tradeoffs between increasing parallelism and incurring overheads

## Slide 18: Outline
Introduction
Background
Characterization
Our proposal: SPAWN
Evaluation
Conclusions

## Slide 19: Design Challenges
PT1
PT2
C1
C3
PT3
C2
overheads
Time
t1
t2
t3
t6
t5
Scenario I
If processed within parent thread.
If processed by launching child kernel.
t4
overheads
overheads
Better not to launch

## Slide 20: Design Challenges
PT1
PT2
C1
C3
PT3
C2
overheads
Time
t1
t2
t3
t6
t5
Scenario I
If processed within parent thread.
If processed by launching child kernel.
t4
overheads
overheads
PT1
PT2
PT3
Scenario II
C1
C3
C2
overheads
overheads
overheads
Better to launch
Better not to launch
Important to decide whether to launch child kernels or not

## Slide 21
Device Runtime
Child CTA Queuing System (CCQS)
  CTA arrival rate (λ), Number of CTAs (n), throughput (T)
  Provide feedback information to update the predictive metrics.
  Launch overhead: a function of the number of child kernels being launched.
  Queueing latency: CTAs waiting in GMU
  Execution time: CTAs executed on PEs.
SPAWN Controller
SPAWN Controller
Child CTA Queuing System (CCQS)
launch kernels
Compute in Parent Thread
PEs
GMU
Launch overhead
Queuing
latency
Execution
time
Feedback
SPAWN

## Slide 22
Whether to launch child kernel or not
  Process the computations by launching a kernel with (x) CTAs:
    Estimated execution time
    t_child = launch overhead + n/T + x/T
    Where
    T = Throughput
    λ = CTA arrival rate
    n = Number of CTAs in CCQS
SPAWN Controller

## Slide 23
Whether to launch child kernel or not
  Process the computation within the thread:
    If a parent thread with (w) computations to process
    Estimated execution time:
    t_parent= w * avg_pwarp_time
    Where
    w = Number of computations to process
    avg_pwarp_time = Average parent warp execution time
  If t_parent < t_child, processing within parent thread. Otherwise launch the child kernels.
SPAWN Controller

## Slide 24: Outline
Introduction
Background
Characterization
Our proposal: SPAWN
Evaluation
Conclusions

## Slide 25
GPGPU-sim v3.2.2
  13 SMXs (PEs), 1400MHz, 5-stage pipeline
  16KB 4-way L1 D-cache, 128B cacheline
  1536KB 8-way L2 cache, 128B cacheline.128KB/Memory Partition
  Greedy-Then-Oldest (GTO) dual warp scheduler
Concurrency Limitations
  Concurrent CTA limit: 16 CTAs/SMX (PE) (208 CTAs in total)
  Concurrent kernel limit: 32 hardware work queues
Evaluation Methodology

## Slide 26
Performance Improvement:
  69% over non-DP (all work done by parent kernel)
  57% over baseline-DP (most work done by child kernels).
  Within 4% of the Best-Offline-Search scenario.
Evaluation
Chart: Speedup
| AMR | BFS-citation | BFS-graph500 | SSSP-citation | SSSP-graph500 | JOIN-uniform | JOIN-gaussion | Mandel | GC-citation | GC-graph500 | MM-small | MM-large | SA-thaliana | Geomean
Baseline-DP | 0.51021 | 0.4598 | 0.8617 | 1.0787 | 2.441 | 0.3848 | 0.25747 | 1.4048 | 1.0056 | 0.99506 | 2.4348 | 3.2779 | 4.3765 | 1.0759
Offline-Search (best) | 2.0982 | 1.0412 | 1.492 | 1.1839 | 2.9927 | 1.3566 | 1.0418 | 1.9745 | 1.0203 | 1.0637 | 2.4348 | 3.9313 | 4.3765 | 1.752
SPAWN | 2.0097 | 0.89853 | 1.569 | 1.1287 | 2.4206 | 1.3126 | 1.0378 | 1.7575 | 1.0179 | 1.1461 | 2.5397 | 3.7461 | 4.383 | 1.6878
More results and discussions are
present in the paper.

## Slide 27: Conclusions
Dynamic parallelism improves parallelism for irregular applications running on GPUs.
Aggressive and hardware-agnostic kernel launching degrades performance because of overheads and hardware limitations.
We propose SPAWN, which makes smart child kernel launching decisions based on the hardware state.
SPAWN improves performance by 69% over non-DP implementation and 57% over baseline-DP implementation.

## Slide 28
Controlled Kernel Launch for Dynamic Parallelism in GPUs
Xulong Tang, Ashutosh Pattnaik, Huaipan Jiang,
Onur Kayiran, Adwait Jog, Sreepathi Pai, Mohamed Ibrahim,
Mahmut T. Kandemir, Chita R. Das
HPCA - 23
Questions?

## Slide 29: Backup Slides

## Slide 30: Workload Distribution
Chart: Time
ii
i
iii
iv
Child CTAs got scheduled and start execution.
Parent CTAs start finishing and relinquish resources for child CTAs.
Resource under utilization due to launch overheads, concurrent kernel limits.

## Slide 31: Evaluation
Chart: Time (~1000 cycles)
Chart: Time (~1000 cycles)
Baseline-DP
SPAWN

## Slide 32: Accuracy
Chart: MM-small
-20% -10% AVG +10% +20%
Chart: BFS-graph500
-20% -10% AVG +10% +20%

## Slide 33: Evaluation
Chart: Time (~1000 cycles)
6000
4000
2000
Saved cycles

## Slide 34: SPAWN
Software support
  Source to source translation.
  Extended API call with local workload parameter.
Hardware support
  Tracking and updating historical execution statistics.
Kernel
Launch
Source to Source Translation
CPU Execution
CUDA Runtime
SPAWN
CUDA
Program

## Slide 35
Launch overhead: from invoking API to kernels being pushed into GMU and ready to start execution.
Queuing latency: Kernels waiting in GMU due to the hardware limitations.
  Maximum number of concurrent running kernels.
  Maximum number of concurrent running CTAs.
  Available hardware resources.
Application
Host
(CPU)
1
Grid Management Unit (GMU)
Pending Kernel Pool
32 Hardware Work
Queues
Stream Queue Management (SQM)
K1
K2
K3
K4
K5
K6
K7
K8
K9
Software Work
Queues
SWQ 1
SWQ 2
SWQ 3
Software Support
Hardware Support
2
3
4
5
CU/SMX
CTA scheduler
CU/SMX
L2 Cache
Interconnect
CU/SMX
CU/SMX
Runtime APIs
Device Runtime APIs
6
3
4
+
+
Background: Hardware Supports DP
6

## Slide 36: Accuracy

## Slide 37: Background
Three key parameters related to child kernel.
  THRESHOLD
  Child kernel dimension (c_grid, c_cta).
  Child kernel execution order (c_stream).
parent (type *workload){
/**each parent threads pick up its workload*/
2. type *local_workload = workload[tid];
3. if (local_workload > THRESHOLD){
4. child<<< c_grid, c_cta, shmem, c_stream>>>(type *local_workload);}
5. else
6. while(local_workload){…}
/**waiting for all children to finish*/
7. cudaDeviceSynchronize();
8. }
1. int main( int argc, char** argv){
2. dim3 p_grid; dim3 p_cta; /**parent kernel dimension*/
/**parent kernel launch*/
3. parent<<< p_grid, p_cta>>>(type *workload); }
1. __global__ void child(*c_workload){
2. …
3. }
(a)
(c)
(b)

## Slide 38
Three key parameters.
  Workload distribution (THRESHOLD)
  Child kernel dimension (c_grid, c_cta).
  Child kernel execution order (c_stream).
Performance
Workload distribution between parent and child
All work in
parent kernel
All work in
child kernels
Observations
  Varying the workload distribution ratio (THRESHOLD) results in significant performance impact.
  The preferred workload distribution ratio for each benchmark, even each input, is different.
Characterization of DP Applications

## Slide 39
BFS-citation
Chart: Percentage of Workload
| 0.01 | 0.05 | 0.13 | 0.28000000000000003 | 0.35 | 0.53 | 0.85
Simulator | 0.9877 | 1.0329 | 1.0372 | 1.0104 | 0.87609 | 0.4598 | 0.13162
K20m | 0.98267 | 1.0119 | 1.0471 | 0.80095 | 0.64807 | 0.057886 | 0.057886
BFS-graph500
Chart: Percentage of Workload
| 0.01 | 0.05 | 0.1 | 0.33 | 0.57999999999999996 | 0.77093772298632102 | 0.90560067530227328
Simulator | 1.0787 | 1.3231 | 1.4764 | 1.3437 | 1.2297 | 0.91271 | 0.8617
K20m | 0.97569 | 1.0631 | 1.2005 | 1.5755 | 1.8592 | 1.2964 | 0.91342
MM-small
Chart: Percentage of Workload
| 1.171875E-2 | 3.3203125E-2 | 0.25 | 0.3125 | 0.48828125 | 0.740234375 | 0.89453125
ss | 1.0024 | 1.0299 | 1.3271 | 1.5611 | 1.795 | 2.0568 | 2.4348
hw | 1.0554 | 1.0649 | 1.2046 | 1.2946 | 1.4499 | 1.6941 | 2.3013
Offline-Search: manually varying the workload distribution ratio by twisting the THRESHOLD parameter.
Characterization of DP Applications

## Slide 40: SPAWN design
Accuracy

## Slide 41
Child CTA Queuing System (CCQS)
  CTA arrival rate (λ), Number of CTAs (n), throughput (T)
  Provide feedback information to update the predictive metrics.
SPAWN Controller
  Cost of launching a child kernel:
    Launch overhead + queuing latency + execution time
  Cost of processing the work in parent thread:
    Iterative execution.
SPAWN Controller
Child CTA Queuing System (CCQS)
launch childs
Compute in Parent Thread
SMXs
GMU
Launch overhead
Queuing
latency
Execution
time
Child kernel launch API
Feedback
SPAWN